Integral Foam & Water Faucet-AC/DC

FFAS8101-AD0500BT0

FEATURES

- Brass body

- Integral sensor Faucet/Soap Dispenser

- Foam soap

- Soap sensor distance:9±2cm;

- Faucet sensor distance:20±15%

- AC 220V or DC 6V(4pcs D size battery)

- Standby energy consumption <2W; working energy consumption <4W

- Soap viscosity range:1-20cp

- Water inlet:G1/2”

- Water pressure:0.05-0.8MPa

- flow rate (L/min):<4.5, at 0.1MPa

- Soap volume ≤ 2mLPF

SPECIFICATIONS

Sensor installed at the spout

Faucet  Reach: 117mm

Faucet  Height:  220mm

FINISHES AVAILABILITY

Chrome (- CP)

AWARDS WON

N/A

SHIPPING WEIGHT

Product net  weight:   3.1kg/set

Product gross  weight:  3.15 kg/set

STANDARDS CRITERIA

QB1334-2013

This document is the property of American Standard. It can neither be reproduced, nor communicated, without authorization.

American Standard reserves the right to change dimensions and specifications without notice, we assume no liability for the use of obsolete dimensions.

# Text boxes

DIMENSIONAL DRAWING